## Slide 1: Digital Electronics and Systems
10a.Synchronous sequential Circuits
Moore FSM

## Slide 2: Introduction
We are going to deal with a general class of circuits in which the outputs depend on the past behavior
of the circuit, as well as on the present values of inputs. They are called sequential circuits.
In most cases a clock signal is used to control the operation of a sequential circuit; such a circuit is called a Synchronous Sequential Circuit.
Synchronous sequential circuits are realized using combinational logic and one or more flip-flops.

## Slide 3: Synchronous Sequential Circuit
The general structure of a Synchronous Sequential Circuit is shown in Figure.
The circuit has a set of primary inputs, W, and produces a set of outputs, Z. The values of the outputs of the flip-flops are referred to as the state, Q, of the circuit.
Under control of the clock signal, the flip-flop outputs change their state as determined by the combinational logic that feeds the inputs of these flip-flops.The combinational logic that provides the input signals to the flip-flops derives its inputs from two sources: the primary inputs, W, and the present (current) outputs of the flip-flops, Q. Thus changes in state depend on both the present state and the values of the primary inputs.Figure indicates that the outputs of the sequential circuit are generated by another combinational circuit, such that the outputs are a function of the present state of the flip-flops and of the primary inputs.

## Slide 4: Classifications
Although the outputs always depend on the present state, they do not necessarily have to depend
directly on the primary inputs.
To distinguish between these two possibilities, it is customary to say that sequential circuits whose outputs depend only on the state of the circuit are of Moore type, while those whose outputs depend on both the state and the primary inputs are of Mealy type.
Sequential circuits are also called Finite State Machines (FSM).The name derives from the fact that the functional behavior of these circuits can be represented using a finite number of states.

## Slide 5: Moore State Machine
Design a circuit that meets the following specification:
The circuit has one input, w, and one output, z.
2. All changes in the circuit occur on the positive edge of a clock signal.
3. The output z is equal to 1 if during two immediately preceding clock cycles the input w was equal to 1. Otherwise, the
value of z is equal to 0.

## Slide 6: Design steps
Draw a state diagram.
Obtain State table.
Obtain State assigned table.
Using k map, obtain the logic expressions for next state variables and output.
Implement the circuit using logic expressions obtained.

## Slide 7: State diagram
The first step in designing a finite state machine is to determine how many states are needed and which transitions are possible from one state to another.
Behavior of a sequential circuit can be described in the form of a pictorial representation called as state diagram, which is a graph that depicts states of the circuit as nodes (circles) and transitions between states as directed arcs.