## Slide 1: Digital Electronics and Systems
Topic : Sum of product and Product of sum

## Slide 2
Literal
Each appearance of a variable, either uncomplemented
or complemented, is called a literal.
Example:
If A is a variable, then literals are A and
For ‘n’ variable function – No: of literals are 2n
Consider a function f (A,B) = AB+
In this function, no: of variables = 2
Maximum no: of literals = 2n = 4

## Slide 3
1. Sum of Product (SOP)
2. Product of Sum (POS)
Product term: Variables are in multiplication format.
Sum term: Variables are in addition format.
Representation of Boolean Expression

## Slide 4
Adding product terms.
This SOP is not in standard form.
Because in the last product term one variable, B is missing.
Standard form SOP is also known as Canonical SOP.
Each individual term in standard SOP is called as minterm.
Sum of product (SOP)

## Slide 5
For SOP / minterm
‘0’ corresponds to complemented variable
‘1’ corresponds to normal variable.
Consider the function,
It consists of 3 variables – A , B & C
General equation for finding number of possible combinations = 2n
n = no: of variables
For 3 variables , no: of combinations = 23 = 8

## Slide 7
Based on this truth table
can be written as:
f = m3 + m5 + m6 + m4
This is the alternate representation of standard SOP.
It can also be represented as

## Slide 8
(1)
(2)

## Slide 9
Equation (2) can be written as
Note: The sequence should be in ABC format