## Slide 1: Digital Electronics and Systems
Topic: Karnaugh Map

## Slide 2
Karnaugh Map ( K-Map)
K-Map is an alternate technique for minimizing Boolean expressions.
It contain boxes called cells.
No: of cells = 2n , where ‘n’ is the number of variables.
Thus a 2-variable map contains 4 cells, 3-variable map contains 8 cells and so forth.

## Slide 6
Representation of truth table on Karnaugh map

## Slide 9
Representing standard SOP on Karnaugh map

## Slide 11
Representing standard POS on Karnaugh map

## Slide 13
Grouping cells for simplification
Grouping is combining adjacent cells.
Two cells are said to adjacent if they confirm single change rule.
The simplification is achieved by grouping adjacent 1’s or 0’s.
When adjacent 1’s are grouped, then we get result in the sum of products form.
When adjacent 0’s are grouped, then we get result in the product of sum form.

## Slide 14
Grouping two adjacent ones (pair)

## Slide 16
In a Karnaugh map the left most column and right most columns are considered to be adjacent

## Slide 20
Grouping 4 adjacent ones (Quad)

## Slide 24
Grouping 8 adjacent ones (Octet)

## Slide 29
A group of two eliminates 1 variable.
A group of four eliminates 2 variables.
A group of eight eliminates 3 variables.