## Slide 1: ARM Instruction Set

## Slide 2: ARM Instruction Set
Instructions process data held in registers and access memory with load and store instructions.
Classification of instructions
Data processing instructions
Data Transfer Instructions - Load-Store instructions
Control flow instructions – Conditional & Branching instructions
S/W interrupt instructions
Program status register instructions

## Slide 3: 1. Data Processing Instructions
Perform arithmetic, logical, move, compare and multiply operations
All operations except multiply instructions are carried out in ALU
Uses 3- address instruction format:
  Eg: ADD R0,R1,R2 ; R0 = R1+R2
All operands are 32 bits wide.
  From register.
  Specified as literals in instruction itself.
Result is 32 bits wide
  Stored in register file.
Most Data Processing instructions can Pre-process one operand
using barrel shifter.
Eg: ADD R0,R1,R2, LSL #2 ; R2 = LSL by 2 position
; R0 = R1+R2

## Slide 4: 1. Data processing
Manipulate data within register
1.1 Arithmetic instructions
1.2 Logical instructions
1.3 Move instructions
1.4 Comparison instruction

## Slide 5: 1.1 Arithmetic Instructions
ADD r0,r1,r2
ADC r0,r1,r2
SUB r0,r1,r2
SBC r0,r1,r2
RSB r0,r1,r2
RSC r0,r1,r2
ADD add
ADC add with carry
SUB subtract
SBC subtract with carry
RSB reverse subtract
RSC reverse subtract with carry
Carry-in is the current value of C bit in CPSR

## Slide 7: 1.2 Bit-wise logical operations
AND r0,r1,r2
ORR r0,r1,r2
EOR r0,r1,r2
BIC r0,r1,r2
BIC
  Bit Clear
  Every ‘1’ in the second operand clears the corresponding bit in the first.

## Slide 9: 1.3 Register- Register movement operations
MOV Rd, N
Rd :destination register
N: can be an immediate value or source register
Example: MOV r7,r5
MVN Rd, N
Move into Rd negated value of the 32 bit value from source (N’).
Example: MVN r7,r5

## Slide 11: 1.4 Comparison
Enables comparison of 32 bit values
  Updates CPSR flags but do not affect other registers
CMP r1,r2 compare
CMN r1,r2 compare negated

## Slide 15: ADD r3,r2,r1, LSL #3
Single instruction.
Second reg operand subjected to shift.
LSL : Logical Shift Left.
Various shift & rotate operations:
  Logical Shift Left (LSL),
  Logical Shift Right (LSR),
  Arithmetic Shift Left (ASL),
  Arithmetic Shift Right (ASR),
  Rotate Right (ROR),
  Rotate Right Extended (RRX)
Shifted Register Operands

## Slide 17: With Barrel shifter
Use of Barrel shifter with arithmetic and logical instructions increases the set of possible available operations.
  Useful for fast multiplication and dealing with lists, table and other complex data structure.

## Slide 20: Multiply instructions
Multiply contents of a pair of registers
  Multiplication by immediate constants not supported.
- long multiply generates 64 bit result
Examples:
 mul r0,r1,r2
Contents of r1 and r2 multiplied and the result is put in r0.
umull r0,r1,r2,r3 ; unsigned multiply long
Unsigned multiplication with result stored in r0 and r1.
Number of cycles taken for execution of multiplication instruction depends upon processor implementation.

## Slide 22: Multiply and Accumulate
Result of multiplication can be accumulated with content of another register
MLA Rd, Rn, Rm, Racc
Rd = (Rn*Rm)+Racc
UMLAL RdLo, RdHi, Rn, Rm
[RdHi,RdLo]=[RdHi,RdLo]+(Rn*Rm)

## Slide 24: Data Transfer Instructions
Transfer data between memory and processor registers
Single register load/store
Data types supported are signed and unsigned words(32 bits), half word, bytes. Eg.
Multiple register load/store
Transfer multiple registers between memory and the processor in a single instruction
Swap
swaps content of a memory location with the contents of a register. For semaphore implementation. Eg. SWP (B)

## Slide 32: Control flow instructions
Determines which instructions next.
  Branch
  Branch Conditions

## Slide 40: ARM Addressing:
Register Indirect addressing.
Value in one register taken as memory address.
  LDR rl , [rm] ; rl = mem[rm]
  STR rl , [rm] ; mem[rm] = rl
Offset addressing:
  Pre-indexed: LDR r0,[r1,#4]
  Pre-indexed with auto-indexing: LDR r0,[r1,#4]!
  Post-indexed: LDR r0,[r1],#4

## Slide 41: Stack Addressing:
Full ascending
    Stack grows up
    Base register  highest addr containing valid item.
Empty ascending
    Stack grows up
    Base register  first empty location above.
Full descending
    Stack grows down
    Base register  lowest addr containing valid item.
Empty descending
    Stack grows down
    Base register  first empty location below.

## Slide 42: Thank You
References:
Text books: ARM System on Chip Architecture, 2nd edition,by Steve Furber ( Chapter 3 & 5)
https://youtu.be/UdY5RkkT7bg?list=PLbRMhDVUMngcJu5oUhgpgYqtOn7DmSfuU
https://youtu.be/yXSTWW0O1LE?list=PLbRMhDVUMngcJu5oUhgpgYqtOn7DmSfuU
https://youtu.be/xYQ60EqTNuo?list=PLbRMhDVUMngcJu5oUhgpgYqtOn7DmSfuU