## Slide 1: AMBA Architecture
High Performance Bus Architecture

## Slide 2: Intro
AMBA stands for Advanced Microcontroller Bus Architecture
What-ever communication we have to do whether internal or external needs to be done with the help of busses!
Making an ad hoc choice in every case consumes design resource and inhibits the reuse of peripheral macro cells.
ARM Limited specified the Advanced Microcontroller Bus Architecture, AMBA, to standardize the on-chip connection of different macro cells.
Notes: What-ever communication we have to do whether internal or external needs to be done with the help of busses!
What is advanced architecture then?
On chip communication standard.

## Slide 3: AMBA Architecture
Different busses within AMBA specification: Advanced High Performance Bus (AHB),Advanced System Bus(ASB), Advanced Peripheral Bus (APB)
High BW external m/y interface or any external device of high BW can be connected to AHB/ASB.
External peripheral devices need to be connected to APB which will be connected with help of an internal bridge with AHB/ASB.

## Slide 4
AMBA Based System
Notes: On chip processor is considered 1st master controller for bus, DMA will be the 2nd master once processor hands over busses to DMA! The APB is generally used as a local secondary bus which appears as a single slave module on the AHB or ASB

## Slide 5: BUS Structure details (1/2)
Advanced High Performance Bus
  Connects high performance system module
  Supports burst mode data transfers
  Split transactions
  Single clock edge
Advanced System Bus (ASB)
  Specifies which protocols needs to be followed

## Slide 6: BUS Structure details (2/2)
Advanced Peripheral Bus (APB)
  Optimized minimal power consumption and reduce interface complexity
  Interface to any peripherals which are low BW and do not require the high performance of a pipelined bus interface.
  Appears as local secondary bus.

## Slide 7: Arbitration
The master, x, issues a request (AREQx) to the central arbiter.
When the bus is available, the arbiter issues a grant (AGNTx) to the master.
Master
Initiates read/write operations by providing address and control information
Only 1 bus master allowed to actively use the bus at any one time
Max of 16 masters allowed.

## Slide 8: Bus Transfers (1/3)
When a master has been granted access to the bus, it issues address and control information to indicate the type of the transfer and the slave device which should respond.
Different signals used in transactions
The bus clock, BCLK. This will usually be the same as mclk, the ARM processor clock

## Slide 9: Bus Transfers (2/3)
Bus transfer direction, BWRITE
Bus protection signals, BPROT[1:0], which indicate instruction or data fetches and supervisor or user access.
The transfer size, BSIZE[1:0], specifies a byte, half-word or word transfer.
Bus lock, BLOK, allows a master to retain the bus to complete an atomic readmodify-write transaction.
The data bus, BD[31:0], used to transmit write data and to receive read data. In an implementation with multiplexed address and data, the address is also transmitted down this bus.

## Slide 10: Bus Transfers (3/3)
Slave States
Bus wait, BWAIT, allows a slave module to insert wait states when it cannot com plete the transaction in the current cycle.
Bus last, BLAST, allows a slave to terminate a sequential burst to force the bus master to issue a new bus transaction request to continue.
Bus error, BERROR, indicates a transaction that cannot be completed. If the master is a processor it should abort the transfer.

## Slide 12: Thank you… 

## Slide 13: References
Furber Textbook
https://www.youtube.com/watch?v=bEF8eXZZt7k&t=3375s
https://www.youtube.com/watch?v=QQY-h0HGHnI
https://www.youtube.com/watch?v=j2NI4AXRs1U
https://www.allaboutcircuits.com/technical-articles/introduction-to-the-advanced-microcontroller-bus-architecture/